## Slide 1
MA2011 MECHATRONICS SYSTEMS INTERFACING
Lecture 1
Prof. Cai Yiyu
College of Engineering
School of Mechanical and Aerospace Engineering

## Slide 2
WHAT IS MECHATRONICS?
First introduced in 1969 by Yasakawa Electric, Japan

## Slide 3: MECHATRONICS DEFINITIONS BY BOOKS
Applied Mechatronics (Samili and Mrad)
“Interdisciplinary engineering field comprising the design and development of smart electromechanical systems."
Design with Microprocessors for Mechanical Engineers (Stiffler)
“Science that integrates mechanical devices with electronic controls"
Introduction to Mechatronics & Measurement Systems
(Alciatore & Histand)
“The interdisciplinary field of engineering dealing with the design of products whose function relies on the integration of mechanical and electronic components coordinated by a control architecture."

## Slide 4: MECHATRONICS DEFINITIONS BY BOOKS
Mechatronics - A Foundation Course (de Silva)
“The synergistic application of mechanics, electronics, and computer engineering in the development of electromechanical products and systems through an integrated design approach."
Mechatronics - Electromechanics and Contromechanics (Miu)
“Crossdisciplinary [field] ... that simultaneously involves mechanics, electronics, and control of computer-integrated electromechanical systems"
Mechatronics (Harshama, Tomizuka & Fukuda)
“The synergistic integration of mechanical engineering with electronics and electrical systems with intelligent computer control in the design and manufacture of industrial products, processes, and operations."

## Slide 5: MECHATRONICS DEFINITIONS BY BOOKS
Mechatronics - Electronics in Products and Processes
(Bradley, et al)
“An integrating theme within the design process [combining] electronic engineering, computing and mechanical engineering"
Mechatronics - Electronic Control Systems in
Mechanical Engineering (Bolton)
“Integration of electronics, control engineering and mechanical engineering"

## Slide 6: MECHATRONICS DEFINITIONS BY BOOKS
Mechatronics System Design (Shetty and Kolk)
“Methodology used for the optimal design of electromechanical products”
Mechatronics Engineering
“Preplanned activity to consider electrical, mechanical, and software constraints over the product life cycle in a simultaneous manner early in the development process"
Mechatronics - Mechanical System Interfacing
(Auslander and Kempf)
“The application of complex decision making to the operation of physical systems"

## Slide 7: MECHATRONICS EDUCATION IN DIFFERENT UNIVERSITIES
University Of Washington (US)
“The integrated study of the design of systems and products in which computation, mechanization, actuation, sensing, and control are designed together to achieve improved product quality and performance."
University Of California At Berkeley (US)
“A flexible, multi-technological approach in the integration of Mechanical Engineering, Computer Engineering, Electronics, and Information Sciences"
Rensselaer Polytechnic Institute (US)
“The synergistic combination of mechanical engineering, electronics, control systems and computers, all integrated through the design process."

## Slide 8: MECHATRONICS EDUCATION IN DIFFERENT UNIVERSITIES
Loughborough University (UK)
"Mechatronics is a design philosophy that utilizes a synergistic integration of Mechanics, Electronics and Computer Technology (or IT) to produce enhanced products, processes or systems."
Johannes Kepler University Linz (AUSTRIA)
“Technical systems operating mechanically with respect to at least some kernel functions but with more or less electronics supporting the mechanical parts decisively"

## Slide 9: MECHATRONICS LEARNING RESOURCES
Mechatronics (Journal)
“The synergistic combination of precision mechanical engineering, electronic control and systems thinking in the design of products and manufacturing processes"
ME Magazine
“The synergistic use of precision engineering, control theory, computer science, and sensor and actuator technology to design improved products and processes" "simply the application of the latest techniques in precision mechanical engineering, controls theory, computer science, and electronics to the design process to create more functional and adaptable products."
Industrial Research and Development Advisory
Committee of the European Community
“Synergistic combination of precision engineering, electronic control and systems thinking in the design of products and manufacturing processes."

## Slide 10
WHAT IS A MECHATRONICS SYSTEM?

## Slide 11: MECHATRONICS SYSTEM
Click image to play video

## Slide 12
PART 1: SYSTEM RESPONSE
This lecture explains how a physical system
responds to its dynamics inputs.

## Slide 13: LEARNING GOALS
  Three main characteristics of a good measurement system of Amplitude Linearity, Phase Linearity, and Adequate Bandwidth.
Fourier series representation of a signal and its applications.
Relationship between an instrument's bandwidth and spectra of its input and output signals.
Dynamic response of zero-, first-, and second-order systems.
System response to step and sinusoidal inputs.
Analogies among mechanical, electrical and hydraulic systems.
1
2
3
4
5
6

## Slide 14
PART 1.1 MEASUREMENT SYSTEMS

## Slide 15: MEASUREMENT SYSTEMS - COMPONENTS
A measurement system
(integral part of mechatronics systems)
consists of 3 components:
A transducer
a device usually converts a physical quantity into a time-varying voltage (called analog signal)
A signal processor
a device can modify the analog signal
A recorder
a device displays or records the signal.
transducer
signal processor
recorder

## Slide 16: MEASUREMENT SYSTEMS - COMPONENTS
INPUT
Physical quantity to be measured is called input to a measurement system.
OUTPUT
Transducer transforms the input into a form compatible with the processor to be processed then becomes the output of a measurement system.
DIFFERENCE
Usually, the input is different from the output of a measurement system.
CHARACTERISATION
A good measurement system is characterised by: phase linearity, amplitude linearity, and adequate bandwidth.

## Slide 17: MEASUREMENT SYSTEMS - DIFFERENCES
Click image to play video
actual
input
signal processor
recorder
output

## Slide 18
PART 1.2 AMPLITUDE LINEARITY

## Slide 19: AMPLITUDE LINEARITY
The output always changes with the same factor times by the
change in the input, i.e.,
where α is the proportional constant (gain).

## Slide 20: AMPLITUDE LINEARITY - REMARKS
If not amplitude linearity, it is difficult to interpret the output
A measurement system usually satisfies amplitude linearity over a limited range of input amplitudes (e.g. spring)
Linear response of a measurement system usually holds for a limited range of the input rate
An ideal measurement system exhibits amplitude linearity for any input amplitude and input rate.
1
2
3
4

## Slide 21: AMPLITUDE LINEARITY
Linear

## Slide 22: AMPLITUDE LINEARITY
Nonlinear

## Slide 23: AMPLITUDE LINEARITY
=20 for 1st pulse and 15 for the 2nd pulse
Nonlinear

## Slide 24
PART 1.3 FOURIER SERIES REPRESENTATION OF SIGNALS

## Slide 25: FOURIER SERIES REPRESENTATION OF SIGNALS
To study bandwidth and phase linearity (applied to frequency components of an input signal), it is necessary to review Fourier series representation of a signal.
Any periodical waveform can be represented as an infinite series of sine and cosine waveforms of different amplitudes and frequencies.
Summing up this infinite series gives the original periodical waveform.
Practically, a finite number of the sine and cosine waveforms can adequately represent a periodical waveform.
1
2
3
4

## Slide 26: FOURIER SERIES REPRESENTATION OF SIGNALS
Let be the fundamental or first (lowest) harmonic frequency defined as
where T is period, f0 is fundamental frequency in Hertz (Hz).
The other sine and cosine waveforms have frequencies of integer multiplying by .
1

## Slide 27: FOURIER SERIES REPRESENTATION OF SIGNALS
The Fourier series representation of a periodical waveform f(t) is
where C0 is the DC component of the signal, An and Bn are coefficients. They are given by
Note: C0 is the average value of the waveform over its period.
2
3

## Slide 28: FOURIER SERIES REPRESENTATION OF SIGNALS
Define
Then
That is, a period waveform can be represented by an infinite series of cosine of single amplitude and phase
4
5

## Slide 29: FOURIER SERIES REPRESENTATION OF SIGNALS

## Slide 30: FOURIER SERIES REPRESENTATION OF SIGNALS
Example: Square waveform with period T
6
7
Then
8
Therefore

## Slide 31: FOURIER SERIES REPRESENTATION OF SIGNALS
individual harmonics
combined harmonics
amp=
amp=
amp=
amp= 0

## Slide 32: FOURIER SERIES REPRESENTATION OF SIGNALS
Individual
Harmonics
ω0
amp = 4/
Individual
Harmonics
3ω0
amp = 4/3
Combined
Harmonics
ω0, 3ω0
+
=
Click image to play video

## Slide 33: FOURIER SERIES REPRESENTATION OF SIGNALS
Individual
Harmonics
ω0
amp = 4/
Individual
Harmonics
3ω0
amp = 4/3
Combined
Harmonics
ω0, 3ω0, 5ω0
Individual
Harmonics
5ω0
amp = 4/5
+
=
+
Click image to play video

## Slide 34: FOURIER SERIES REPRESENTATION OF SIGNALS
Plotting spectrum
When plotting spectrum for a signal represented by a Fourier series, use single-amplitude by equation (5),
signal
time domain
time
spectrum
frequency
frequency domain
amplitude
1.5
4/
4/
0

## Slide 35
PART 1.4 BANDWIDTH AND FREQUENCY RESPONSE

## Slide 36: BANDWIDTH AND FREQuENCY RESPONSE
It is important to estimate spectrum of a signal when choosing a measurement system
Ideal measurement system replicates all frequency components of an input signal
Practical measurement system has limitation in reproducing all frequencies.
1
2
3

## Slide 37: BANDWIDTH AND FREQuENCY RESPONSE
Common scale used to measure fidelity of a measurement system’s reproduction at different frequencies is the decibel scale:
where Ain and Aout are input and output amplitudes of a harmonic.
9

## Slide 38: BANDWIDTH AND FREQuENCY RESPONSE
Frequency response curve or Bode plot plots Aout/Ain vs. input frequency
amplitude ratio
bandwidth
frequency
1.000
0.707
(-3dB)

## Slide 39: BANDWIDTH AND FREQuENCY RESPONSE
Bandwidth is the range of the frequencies where the input is not attenuated by more than -3dB, i.e.
where and called corner or cut-off frequencies.
Why -3dB? This comes from half of output power over input power,
i.e.,
So, bandwidth is proportional to fidelity of a measurement system.
10
11

## Slide 40: BANDWIDTH AND FREQuENCY RESPONSE
Example: Calculating output amplitude given a measurement frequency response curve: -the input signal spectrum is
the output amplitude is calculated as
12
13

## Slide 41: BANDWIDTH AND Frequency RESPONSE
input signal spectrum
frequency
10
frequency
measurement system
frequency response
frequency
output signal
spectrum
Example: Calculating output amplitude given a measurement frequency response curve: -the input signal spectrum is
the output amplitude is calculated as
12
13