## Slide 1: MA2012 Introduction to Mechatronics Systems Design (Circuit 2)
A/P Ang Wei Tech
  Email: wtang@ntu.edu.sg
  Tel: 6790 4911
  Office: N3-01-04

## Slide 2: Components
Circuit 2A:
  Servomotor
  Stepper motor
  DC motor
  DC motor + Encoder
Circuit 2B:
  16-key Hexadecimal Keypad
  74C922 Keypad Encoder
  Liquid Crystal Display (LCD)

## Slide 3: Circuit 2A

## Slide 4: Circuit 2A

## Slide 5: Servo Motor
The drive flange can rotate ½ revolution
It is driven by high pulse (Logic 1) called ‘Mark’
0 to 180
(-90 to +90)
Mark
Space

## Slide 6: Servo Motor
0.5
1.0
1.5
2.0
2.5
Mark Length (ms)
Drive flange rotation ()
0
45
90
135
180
Safe range

## Slide 7: Stepper Motor
RS 440-420
Stepper Motor Construction
Rotor & Stator Configuration
White
Brown
Red
Yellow
Blue
Brown
Windings
Stator

## Slide 8: Stepper Motor Working Principle

## Slide 9: Stepping Sequence (Wave-Drive / Single Phase)
Step | A (1) | B (3) | A’ (2) | B’ (4)
1 | On |  |  | 
2 |  | On |  | 
3 |  |  | On | 
4 |  |  |  | On
Unipolar stepper motor
Step 1, 2, 3, 4, 1 … : CCW
Step 1, 4, 3, 2, 1 … : CW
Step 1

## Slide 10: Stepping Sequence (2 Phase Full Step)
Step | A (1) | B (3) | A’ (2) | B’ (4)
1 | On | On |  | 
2 |  | On | On | 
3 |  |  | On | On
4 | On |  |  | On
Unipolar stepper motor
Step 1, 2, 3, 4, 1 … : CCW
Step 1, 4, 3, 2, 1 … : CW
Step 1

## Slide 11: Stepping Sequence (2 Phase Half Step)
Step | A (1) | B (3) | A’ (2) | B’ (4)
1 | On | On |  | 
1.5 |  | On |  | 
2 |  | On | On | 
2.5 |  |  | On | 
3 |  |  | On | On
3.5 |  |  |  | On
4 | On |  |  | On
4.5 | On |  |  | 
Step 1, 1.5, 2, 2.5, 3, 3.5, 4, 4.5, 1 … : CCW
Step 1, 4.5, 4, 3.5, 3, 2.5, 2, 1.5, 1 … : CW
4.5
4

## Slide 12: Step Sequence – Higher Resolution
Double the number of poles will half the step size

## Slide 13: Stepper Driver UCN5804B
Three types of drive:
  Wave drive (A-B-C-D)
  Two phase full step (AB-BC-CD-DA)
  Two phase half step (A-AB-B-BC-C-CD-D-DA)
See data sheet for more details

## Slide 14: Motion Control Fundamental
Power = VI = 
DC motor control
  Voltage controls velocity: V  
  Current controls torque: I  
  Rated power
    Motor running at rated speed, drawing rated current
    Motor reliably, performance, etc. is guaranteed by manufacturer

## Slide 15: Pulse Width Modulation
If switch is always on, lamp receives 9V and light up to the rated brightness
If switch is 50% on and 50% off very quickly (1 – 200 kHz), lamp receives an equivalent of 4.5 V, thus only 50% of rated brightness

## Slide 16: Pulse Width Modulation
Duty cycle = % of on = % of rated power (assuming constant current)
Digital-to-Analog Converter (DAC) is expensive
  Not many MCU are equipped with a DAC
Solution: PWM

## Slide 17: DC Motor Control with H-Bridge
Clockwise rotation
Counterclockwise rotation
See datasheet DRV8833
Slow deceleration
Fast deceleration

## Slide 18: Geared Motor with Encoder
Encoder Resolution: Hall Resolution 11x Speed Reduction Ratio 34 = 374 PPR (pulse per revolution)
What is the encoder resolution in degree per pulse?
Incremental (Quadrature) encoder working principle:
  ChA leads ChB by 90: CCW
  ChA lags ChB by 90: CW
+ve
-ve
Rotation
- -
++
Encoder

## Slide 19: Circuit 2B

## Slide 20: Circuit 2B

## Slide 21: 16-Key Hexadecimal Keypad
8 outputs

## Slide 22: 74C922 Keypad Encoder
8 inputs for Keypad
4 outputs
Data Available – Key entry

## Slide 23: 74C922 Keypad Encoder
Position = A + 2.B + 4.C + 8.D

## Slide 24: Keypad Example
Read a keypad and print out the key to serial monitor
if(digitalRead(KB_DataAvailable))
k=ka+kb*2+kc*4+kd*8;
char keys[] = {'1','2','3','F',
'4','5','6','E',
'7','8','9','D',
'A','0','B','C'};

## Slide 25: Liquid Crystal Display (LCD)
16 x 2 Character Module
See <LiquidCrystal.h> library

## Slide 26: Exercise 2-1: Gantry Crane
Write a program to perform the follow tasks:
  An operator uses the potentiometer to control the servomotor which positions the hoist of a Gantry Crane over an object placed around the mid point across the width of the crane (i.e. servomotor position between 80-100 deg).
  When the hoist is in position, activating the pushbutton shall rotate the DC motor to raise/lower the cable to grab the object. Releasing the pushbutton shall stop the DC motor.
  A toggle switch is used to control the direction of the cable:
  HIGH = raising; LOW = lowering.
  The pushbutton shall not activate the DC
  motor if the servomotor is not in position
  (outside 80-100 deg)

## Slide 27: Exercise 2-2: Gantry Crane 2
With reference to Ex.2-1
  Replace the Servomotor with a DC Motor with encoder.
  Replace the DC motor with a Stepper Motor.

## Slide 28: Exercise 2-3: Calculator
Write a program to perform the following tasks:
  Pressing 2 consecutive keys of ‘F’ turn the keypad into a calculator:
    ‘A’ ≡ + (add), ‘B’ ≡ - (subtract), ‘C’ ≡ * (multiply), D ≡ / (divide), E ≡ = (equal)
    The calculator should perform 3-digit (0-999) integer arithmetic, i.e. no decimal digits, e.g. 1.5  1.0
    The LCD should display digits and/or symbols consistent with a normal calculator. You may apply appropriate assumptions.
  Pressing keystrokes of ‘F’ + ‘E’ turn off the calculator function and return to displaying entered keys