## Slide 1: MA2012 Introduction to Mechatronics Systems Design (Circuit 3)
A/P Ang Wei Tech
  Email: wtang@ntu.edu.sg
  Tel: 6790 4911
  Office: N3-01-04

## Slide 2: Components
Accelerometer ADXL345
Logic Level Converter
  Switches between 3.3V and 5V
Bluetooth Module HC-05

## Slide 3: Accelerometer ADXL-345
Measures acceleration in 3 principal axes
Supports SPI and I2C protocols

## Slide 4: Circuit 3A-SPI & 3B-I2C

## Slide 5: Circuit 3a SPI

## Slide 6: Serial Peripheral Interface (SPI)
Interface bus used to send data between microcontrollers and small peripherals such as shift registers, sensors, and SD cards
3 lines for communication
  Shared/Serial Clock (SCK)
  Master Out Slave In (MOSI) or Slave Data In (SDI)
  Master In Slave Out (MISO) or Slave Data Out (SDO)
1 slave select (SS) line

## Slide 7: Serial Peripheral Interface (SPI)
1 slave select (SS) line for each slave device
  Normally held high to disconnect the slave
  Brought to LOW to initiate the communication
  Brought to HIGH after communication
Total number of I/O pins required = 3 + n n = number of slave devices

## Slide 8: Serial Peripheral Interface (SPI)
Basic process:
Set the SS pin LOW for the targeted slave device
Toggle SCLK (square wave) at a speed ≤ transmission speed supported by the slave device
For each clock cycle, master sends 1 bit on MOSI and receives 1 bit on MISO
Continue until data transmission is complete, and stop toggling the clock line
Set SS pin to HIGH

## Slide 9: Serial Peripheral Interface (SPI)
#include <SPI.h>
Arduino Uno:
  11 (MOSI)
  12 (MISO)
  13 (SCK)
  10 (SS)
Library Functions
SPISettings(speed,MSB/LSB,mode)
SPI.begin()
SPI.beginTransaction(settings)
SPI.transfer() //read, write

## Slide 10: SPISettings(speed,MSB/LSB,mode)
Speed = rated speed of slave
MSB first or LSB first
Mode :
Mode | Clock Polarity (CPOL) | Output Edge | Data Capture
SPI_MODE0 | Low at idle | Falling | Rising
SPI_MODE1 | Low at idle | Rising | Falling
SPI_MODE2 | High at idle | Rising | Falling
SPI_MODE3 | High at idle | Falling | Rising

## Slide 11: Configuration
Pg15: DEVID(0x00)
  Sensor ID
Pg16: POWER_CTL (0x2D)
  0b 0000 1000 (0x08)

## Slide 12: SPI Write
Datasheet pg9
MSB: Write (0)
Followed by 7 bit registry address

## Slide 13: SPI Read
Datasheet pg9
MSB: Read (1)
Followed by 7 bit registry address

## Slide 14: SPI Read Example:
Read from DATAX0
Why are sending 0xF2 instead of 0x32?
  MSB: 1 = Read, 0 = Write
  0b 0011 0010 (0x32): Register Address
  0b 1111 0010 (0xF2):
    MSB=1 to indicate read
    MB=1 to indicate multiple bytes (pg8)

## Slide 15: x=SPI.transfer(0) | SPI.transfer(0)<<8;
H | G | F | E | D | C | B | A | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
MSB
DATAX : 0x32 to 0x33 (pg18)
  0x32
  0x33
When reading, 0x32 is send out first
  1st read : 0b 8765 4321
  2nd read: 0b HGFE DCBA
8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
H | G | F | E | D | C | B | A

## Slide 16: Circuit 3b I2C

## Slide 17: Inter-Integrated Circuit (I2C)
Only 2 signals lines:
  Clock signal (SCL)
  Data signal (SDA)
Each device must have a unique address
Each signal line requires a pull-up resistor to restore the signal to HIGH when no device set it LOW.

## Slide 18: Inter-Integrated Circuit
Basic steps:
  Master sends a Start bit
  Master sends a 7-bit slave address of intended device
  Master sends a Read (1) or Write (0) bit depending on application
  Slave responds with an “acknowledge”, i.e. ACK bit (0)
  In Write mode, master sends 1 byte of information (command or data) at a time, and slave respond with ACKs. In Read mode, master receives 1 byte of information at a time and sends an ACK to the slave after each byte
  When communication has been completed, master sends a Stop bit

## Slide 19: Inter-Integrated Circuit (I2C)
#include <Wire.h>
Arduino Uno:
  A4 (SDA)
  A5 (SCL)
Library Functions
Wire.begin()
Wire.beginTransmission(ADR)
Wire.endTransmission()
Wire.write(DATA)
Wire.requestFrom(ADR,byte_size)
Wire.read() //read 1 byte data

## Slide 20: I2C to Accelerometer
Datasheet pg10
Data transferred in 8 bits (MSB first)
Slave Address :
  0x1D when SDO/ALT ADDRESS to HIGH
  0x53 when SDO/ALT ADDRESS to LOW

## Slide 21: I2C Read Data
Datasheet pg18
Acceleration
  DATAX0 : 0x32
  DATAX1 : 0x33
  DATAY0 : 0x34
  DATAY1 : 0x35
  DATAZ0 : 0x36
  DATAZ1 : 0x37

## Slide 22: Read Data
Wire.requestFrom(address, quantity)
Wire.requestFrom(address, quantity, stop)
Parameters
address: the 7-bit address of the device to request bytes from
quantity: the number of bytes to request
stop : boolean. true will send a stop message after the request, releasing the bus. false will continually send a repeated start after the request, keeping the connection active.

## Slide 23: Circuit 3c UART & Bluetooth

## Slide 24: Circuit 3c UART & Bluetooth

## Slide 25: Universal Asynchronous Receiver/Transmitter (UART)
One to one Communication
Arduino Uno: 0 (RX), 1(TX) (built in UART)
#include <SoftwareSerial.h>
  For use with other digital pins
SoftwareSerial(rxPin, txPin, inverse_logic) | print() , println()
begin(speed) | write() //send as raw bytes
available() | read() //read one byte
listen() | 

## Slide 26: Universal Asynchronous Receiver/Transmitter (UART)
Organise data into packets, each contains:
  1 start bit (LOW)
  5 – 9 data bits
  1 optional parity bit
  1 – 2 stop bit (HIGH)
Read data according to baud rate (bit/s)

## Slide 27: HC-05 (Bluetooth) on zs-040
Use UART to communicate with Arduino

## Slide 28: Connect with Bluetooth
Phone Use: “Serial Bluetooth Terminal” from Google Play
PC Use: “Bluetooth Serial Terminal” from Microsoft Store
Connect to your Bluetooth device
Send message

## Slide 29: Using Bluetooth with Phone
Select device that you want to connect
Click to connect
Blue text by phone
Green text by Arduino Serial Monitor

## Slide 30: Using Bluetooth with PC

## Slide 31: Ex.3-1 Inclinometer
Write a program to perform the following tasks which involves the ADXL345 accelerometer
  Using SPI protocol:
    If accelerometer is horizontal (tilt <=  10), set the on-board LED to blink
      Display “0 degree” on Serial Monitor
    If ABS (tilt) > 10, turn off the LED
      Display the tilt angle (to the nearest 0.5 degree) on Serial Monitor, e.g. “15.0 degrees” or “-73.5 degrees”
  Repeat using I2C protocol

## Slide 32: Ex.3-2 Voltage Matching
Write a program to perform the following tasks:
  MCU1:
    Connect a potentiometer to one of the unused Analog Input pins
    Use Serial communication protocol to transmit voltage output of the potentiometer to MCU2
  MCU2:
    Use a voltage divider circuit to input 2.5V into one of the unused Analog Input pin
    If the voltage value received from MCU1 is 2.5V  0.1, set the on-board LED to blink
      Use Serial communication protocol to transmit 5 characters to MCU1: “B”, “I”, “N”, “G”, “O”
  MCU1:
    Use Serial monitor to display the word “BINGO”