## Slide 1
MA2012 INTRODUCTION TO MECHATRONICS SYSTEMS DESIGN
Lecture 1
Prof Ang Wei Tech
College of Engineering
School of Mechanical and Aerospace Engineering

## Slide 2: TEXTBOOKS, LECTURE SLIDES AND HANDOUTS
Textbooks
  Introduction to Mechatronics and Measurement Systems, 4th Ed., D. G. Alciatore & M. B. Histand, McGraw Hill, 2012
  Exploring Arduino, Jeremy Blum, Wiley, 2013
Lecture Slides & Lab Handouts
  Will be posted on NTULearn in due course

## Slide 3: COURSE OBJECTIVES
To understand and develop mechatronics systems using microcontrollers to interface with various types of input devices, displays and actuators
To gain hands-on experience and knowledge of mechatronics system design and development
To interpret tasks into technical specifications
To read and understand component data sheets

## Slide 4: SCOPE
We shall learn sufficient details to understand the components of a mechatronics system and the techniques required to accomplish mechatronic tasks effectively
We shall not learn all the low level details, architecture and manufacturing process of the electronic/electrical components as required by Electrical & Computer engineers

## Slide 5: MECHATRONICS
Mecha-nical + Elec-tronics
  A term coined in Japan in 1960s
A interdisciplinary field of engineering dealing with the design of products whose function relies on the integration of mechanical and electronics components coordinated by a control architecture

## Slide 6: SYSTEM
  A combination of related parts organized into a complex whole
Definition
System science
System engineering
  An interdisciplinary field of science that studies the nature of complex systems
  An interdisciplinary field of engineering that focuses on how complex systems should be designed, engineered and managed

## Slide 7: SYSTEM
Signal Processor
Transducer
Recorder
  A system that presents an observer with a numerical value that represents the state or change of a variable of a process, machine or system being measured
Measurement system

## Slide 8: SYSTEM
Actuation system
  A system that converts one form of energy (e.g. electrical, chemical, etc.) to another to perform mechanical work (e.g. movement, heat, etc.).
Actuation System
e.g. Motor
Rotation
Input
Output
Electrical Power

## Slide 9: SYSTEM
Control system
  A system to modify one or more measurable parameters of a plant or process to achieve desired output(s), E.g. A central heating system
  Input: electrical power; Actuation system: heating coil, blower; Plant: environment / room; Measurement system: temperature sensor; Output: desired temperature
Plant / Process
Actuation System
Control System
Input
Desired Output
Measurement System

## Slide 10: MECHATRONIC SYSTEM COMPONENTS

## Slide 11: MECHATRONIC SYSTEM COMPONENTS
Mechanical system
  Actuators
    Motors (AC, DC, Stepper, Servo, Voice Coils, etc.)
    Hydraulics, Pneumatics, Solenoids
    Piezoelectric, other smart materials
    Others: Heating/Cooling elements

## Slide 12: MECHATRONIC SYSTEM COMPONENTS
Mechanical system
  Sensors
    Switches: ON/OFF
    Potentiometer, Encoder: Position or displacement
    Inertial Sensors:
      Accelerometer: Acceleration; Rate Gyroscope: Angular velocity
    Thermocouple: Temperature
    Strain gage: Deflection
    Photoelectrics: Light intensity

## Slide 13: MECHATRONIC SYSTEM COMPONENTS
Mechanical system
  System model, e.g. 1st or 2nd order system
1st order
2nd order

## Slide 14: MECHATRONIC SYSTEM COMPONENTS
Mechanical system
  Static & Dynamic responses
1st order
2nd order
Step response

## Slide 15: MECHATRONICS SYSTEM COMPONENTS
Input signal conditioning and interfacing
  Discrete circuits – circuits made up of discrete components (e.g. resistors, capacitors, etc.)
  Amplifiers – to amplifier signal to improve signal to noise ratio (SNR)
  Filters – to get rid out unwanted signal contents, e.g. highpass, lowpass, bandpass, bandstop, etc.
  Analog-to-Digital Converter

## Slide 16: MECHATRONICS SYSTEM COMPONENTS
Output signal conditioning and interfacing
  Filters, Op-amps, Digital-Analog Converter (DAC), etc.
Light Emitting Diodes (LED)
Liquid Crystal Display (LCD)
GRAPHICAL DISPLAYS

## Slide 17: MECHATRONICS SYSTEM COMPONENTS
Digital control architectures
  The ‘brain’ of the system, usually a microcomputer
  Microprocessor (MPU) = Central Processing Unit (CPU) on a single integrated-circuit (IC) chip
  Microcomputer = MPU + Memory + I/O unit
  Microcontroller (MCU) = Microcomputer in a single IC chip
  Function: Logic, Arithmetic, Control, Timing & Sequencing, Communications, etc.

## Slide 18: EMBEDDED SYSTEMS
Microcontroller for a single purpose (not single function)
Examples
  Consumer Products: Mobile Phone, Washer, Fridge, A/C
  Healthcare Products: Treadmills, Blood Glucose Metre, etc.
  Automobile System Controller & many more
Advantages
  Cheap, small, low power consumption
Disadvantages
  Inflexible, no or limited expandability

## Slide 19: GENERAL PURPOSE COMPUTERS
Examples
  PC, Macintosh, Workstation, PDA, Smartphone, etc.
Advantages
  Flexibility – capable of running many software and interface with lots of devices
  Expandability / Scalability – software & hardware upgradeable
Disadvantages
  Complexity – to cater for flexibility & expandability
  Cost – $100’s to $1,000’s
  Power Consumption – high
Outnumbered by embedded systems >100:1

## Slide 20: BASIC COMPUTER STRUCTURE
All computers contain 3 basic units:
  Central Processing Unit (CPU)
    Arithmetic & Logic Unit (ALU)
    Control Unit
  Memory Unit
    Internal – Random Access Memory (RAM), Read-only Memory (ROM)
    External – Hard Disk, Tape, etc.
  Input/Output (I/O) Unit
    Input Unit – Mouse, K/B, Analog/Digital Converter (ADC)
    Output Unit – Display, Digital/Analog Converter (DAC)

## Slide 21: BASIC COMPUTER STRUCTURE
Redo this figure and remove the numbers in the arrows.
Input
Arithmetic/logic unit
(ALU)
Control
Memory
Output
From
outside
world
To
outside
world
Central processing unit
(CPU)

## Slide 22: CENTRAL PROCESSING UNIT (CPU)
CPU = ALU + Control unit
Arithmetic and Logic Unit (ALU)
  Arithmetic: +, –, x, , etc.
  Logic: OR, AND, NOT, NOR, NAND, XOR, etc.
  Result of ALU is usually stored in the Accumulator register (More later)
Control Unit
  Directs the operation of all parts of computer by providing timing and control signals
  Fetches, decodes, and executes the instructions in memory

## Slide 23: MEMORY
A memory cell is a device or circuit used to store a single bit (“1” or “0”). E.g. FFs, magnetic core, disk
A memory word is a group of memory cells
Internal memory (a.k.a. main or working memory)
  Highest speed memory
Function
  Store programs for sequenced execution
  Store data for output at required time
Types of memory
  RAM, ROM, EEPROM

## Slide 24: SOFTWARE
microprogram
  Collection of instructions that control the timing and control logic of all components of MPU
  Built into the MPU by chipmaker & cannot be modified by programmers
FIRMWARE
  Software programmed into the Read-Only Memory (ROM) of a MCU for the execution of functions of a device
  Programmed by device manufacturer and cannot be modifier by users
program
  Software loaded into the Random Access Memory (RAM) of a GP computer
  Programmed by software developer (not necessarily device manufacturer) and cannot be modified by users

## Slide 25: MECHATRONIC SYSTEM COMPONENTS

## Slide 26: MECHATRONIC SYSTEM EXAMPLE
A typical car contains > 50 MCUs!
Active stabilization
Air bag system
Automatic gearbox
Combustion engine control
Entertainment & Navigation systems
Climate control
Seatbelt alert system
Door security system
Fuel & fluid alert system
Speed control system
ABS braking

## Slide 27: MECHATRONICS SYSTEM EXAMPLE
Inkjet Printer
  How many actuators are there? What type?
  How many sensors are there in the paper feeding mechanism? In the print head mechanism?
  What is the control architecture?

## Slide 28: MECHATRONICS SYSTEM EXAMPLE
Inkjet Printer
  Actuators:
    Stepper motor to drive print head mechanism
    Stepper motor to drive paper feeding mechanism
    Stepper motor to park print head mechanism (some models)
    Ink firing at nozzles
      Piezoelectric (Epson) or Thermal resistor (Canon & HP)

## Slide 29: MECHATRONICS SYSTEM EXAMPLE
Inkjet Printer
  How many sensors are there in
  the paper feeding mechanism?
  In the print head mechanism?

## Slide 30: MECHATRONICS SYSTEM EXAMPLE
Inkjet Printer
  Sensors in paper feeding mechanism
    Proximity sensors or limit switch to detect presence of paper
    Proximity sensors to detect paper loaded in position at the start of a print
  Sensors in print head mechanism
    Linear encoder for precision positioning of print head
    Limit switch to detect print head in parked position

## Slide 31: MECHATRONICS SYSTEM EXAMPLE
Inkjet Printer
  What is the control
  architecture?

## Slide 32: MECHATRONICS SYSTEM EXAMPLE
Inkjet Printer
  Digital control architecture
    Microcontroller based
    Communications:
      USB (parallel) port
      Bluetooth
      LAN port
      WiFi
    Graphics Display
      Simple LCD to high definition LED

## Slide 33: MECHATRONICS SYSTEM EXAMPLE
robot
Serial Robot
Parallel Robot

## Slide 34: MECHATRONICS SYSTEMS DESIGN STEPS
To understand the task
To decide on the type of mechatronics component: digital control architecture, actuators, sensors, etc.
To look for the components with the suitable specifications
To ensure compatibility of components: interfacing
To construct hardware prototype
To programme software / firmware

## Slide 35: SUMMARY
What is a Mechatronics system?
Systems – definition and example
Mechatronics System Components
Mechatronics System Examples
Mechatronics System Design Steps

## Slide 36: ATTRIBUTIONS
By KaiLumtec (Own work) [CC BY-SA 3.0 (http://creativecommons.org/licenses/by-sa/3.0)], via Wikimedia Commons
By oomlout (16x2 LCD Display - LCDD-01) [CC BY-SA 2.0 (http://creativecommons.org/licenses/by-sa/2.0)], via Wikimedia Commons