## Slide 1
MA2012 INTRODUCTION TO MECHATRONICS SYSTEMS DESIGN
Lecture 2
Prof Ang Wei Tech
College of Engineering
School of Mechanical and Aerospace Engineering

## Slide 2: RECAP
What is a Mechatronics system?
Systems – definition and example
Mechatronics System Components
Mechatronics System Examples
Mechatronics System Design Steps

## Slide 3: MECHATRONIC SYSTEM COMPONENTS

## Slide 4: MICROCONTROLLER
Microcontroller (MCU) is a microcomputer (CPU + Memory + I/O) in a integrated circuit chip
In this course, we use Arduino UNO

## Slide 5: ARDUINO UNO MCU SPECIFICATIONS
Microcontroller | ATmega328
Digital I/O | 14 (of which 6 provide PWM output)
Analog Input | 6
Microprocessor Speed | 16 MHz
Memory: Flash SRAM EEPROM | 32 kB 2KB 1KB
Voltage: Operating Input | 5 V 7-12 V
Physical: Dimension Weight | 68.6 x 53.4 mm 25 g

## Slide 6: ARDUINO UNO COMPONENTS
ATMega328 MCU

## Slide 7: ARDUINO UNO MCU
Arduino Uno is a MCU, ATmega328 is also a MCU. What happened?
  Arduino uses OEM (Original Equipment Manufacturer) microcontrollers and reengineers them into different architectures (i.e. memory, bus, I/O configuration, communication integrated chips (IC), etc.) for their own customized needs

## Slide 8: NUMBER OF BITS
ATmega328 is a 8-bit MCU, i.e. Arduino Uno is a 8-bit MCU
  Amount of data processed at one time = 8 bits = 1 byte
16 -bit MCU would process twice amount of data
  32-bit  4x; 64-bit  8x
N-bit MCU has
  N-bit word (variable) size, 2N different possible values
  N-bit instruction size, 2N number of instructions / commands

## Slide 9: PROGRAM EXECUTION SPEED
Arduino Uno microprocessor speed = 16 MHz
Program Execution Speed ≠ Driven Clock Speed (Microprocessor speed)
Microprocessor runs at a higher frequency than all other components, i.e. memory, bus, I/O, etc.
Program execution speed is heavily influenced by the slowest component(s)

## Slide 10: COMPUTER GENERAL KNOWLEDGE QUIZ #1
What is the processor speed of your mobile phone CPU?
How many bits does the CPU have?
How about your laptop?

## Slide 11: MOBILE PHONE SPECIFICATIONS

## Slide 12: LAPTOP SPECIFICATIONS

## Slide 13: MEMORY
A memory cell is a device or circuit used to store a single bit (“1” or “0”)
A memory word is a group of memory cells
Internal memory (a.k.a. main or working memory)
  Highest speed memory
Function
  Store programs for sequenced execution
  Store data for output at required time
Types of memory
  RAM, ROM, EEPROM, Flash

## Slide 14: RANDOM ACCESS MEMORY (RAM)
Any memory device that can go directly to an address without having to sequence through other locations
Volatile
  Data gone when system loses power
Variables and I/O data are stored in RAM when arithmetic & logic operations are performed on them
RAM in Arduino Uno
  Capacity = 2 kB
  Type: Static RAM

## Slide 15: STATIC RAM VS DYNAMIC RAM
  Semiconductor RAM device that consists essentially of flip-flop registers and the necessary circuitry for decoding
  Information will remain valid as long as power is on
  Advantages
    Access speed, circuitry simplicity
SRAM
  Memory devices that store binary data by charging the gate capacitances of Metal Oxide Semiconductor (MOS) transistors
  Refreshing or periodically recharging (every ~4 ms) is required
  Advantages
    Cost, density, low power consumption
dRAM

## Slide 16: READ-ONLY MEMORY (ROM)
Semiconductor memory device design primarily for having data read from them
Data cannot be changed during operation
Non-volatile
  Data is not lost when power is off
Program vs write
  Programming refers to a procedure of putting data into memory for nonvolatile storage
  Writing means an instruction that send data to an address in RAM or external storage

## Slide 17: ELECTRICALLY ERASABLE PROGRAMMABLE ROM (EEPROM)
  Semiconductor ROM device with which the user can erase and reprogram the contents of memory as many times as desired
  Exposure to UV lights erases information on the entire memory chip (all 1’s)
Erasable programmable rom (eprom)
eEprom
  Semiconductor ROM device with which the user can erase and reprogram individual locations by the application of appropriate voltage levels and pulse durations
EEPROM in Arduino Uno = 1 kB

## Slide 18: FLASH MEMORY
A type of EEPROM, i.e. non-volatile
Erasable and programmable a block of data instead of a bit
Can be used as ROM (Flash Bios), Disk Drive (USB drive, SD card, Solid State Drive, etc.) or RAM (Flash RAM)
Advantages vs
  EEPROM – Versatility, can be used as RAM
  RAM – As fast as DRAM, non-volatile
  Disk Drive – Speed, no moving parts (solid state)
Flash Memory in Arduino Uno = 32 kB

## Slide 19: ARDUINO UNO MEMORY SUMMARY
RAM (2 kB)
  To store run-time data
EEPROM (1 kB)
  To store settings and fixed parameters between resets
Flash Memory (32 kB)
  Act like a hard drive to store programs & data
  The programs which you are going to write are store here
  0.5 kB is reserved for Bootloader program (Details later)

## Slide 20: COMPUTER GENERAL KNOWLEDGE QUIZ #2
What much memory does your mobile phone have?
What type of memory?
How about your laptop?

## Slide 21: MOBILE PHONE SPECIFICATIONS

## Slide 22: LAPTOP SPECIFICATIONS

## Slide 23: SDRAM – SYNCHRONOUS DYNAMIC RAM
DRAM which synchronous with system bus
Main reasons to use DRAM
  Capacity and power consumption are more important factors than access speed
System or Frontside Bus
  Parallel conductor lines which
  connects CPU to other components
  64-bit processor needs bus to be
  64-bit wide, i.e. 1 bit of info per line
Other comp-onents
Comp-onents on other bus types

## Slide 24: SDRAM – SYNCHRONOUS DYNAMIC RAM
  Data transfer at both the positive going and negative going transitions, hence double data rate
  DDRn is DDR generation n
  LPDDR is Lower Power DDR for mobile devices
  GDDR is graphics DDR for
  graphics card
Double Data Rate (DDR)

## Slide 25: COMPUTER GENERAL KNOWLEDGE QUIZ #3
When you download a new game on your mobile phone, where is the game stored?
(A) RAM, (B) Flash Memory, (C) Neither
When you are playing a game of Angry Bird, where does the CPU store the current states of the game, i.e. how many birds or pigs left?
Where does the CPU store the high score?
(A) RAM, (B) Flash Memory, (C) Neither

## Slide 26: ARDUINO UNO COMPONENTS
Digital I/O
ATMega328 MCU
ADC
Power & Auxiliary pins
DC Input
USB Input
Reset button

## Slide 27: OTHER COMPONENTS
General or Digital Input / Output pins
  Total = 14
  Digital signal has two states:
    LOW (0)= 0 V
    HIGH (1) = 5 V
Analog-to-Digital Converter (ADC) pins
  Total = 6
  To convert analog (continuous) signals into their digital equivalents
  More in Lecture 3
Power Supply
  Accept 6-20 VDC input, 7-12 VDC is recommended

## Slide 28: ARDUINO IDE (INTEGRATED DEVELOPMENT ENVIRONMENT)
Can be downloaded from
https://www.arduino.cc/en/Main/Software
Programming in C++ language

## Slide 29: CONNECTING PC TO ARDUINO BOARD
Upload button
USB Cable
USB Input
USB port
Clicking the Upload button shall upload the program to the Flash Memory of Arduino Uno

## Slide 30: BOOTLOADER PROGRAM
A program to “boot-up” or “bootstrap” the computer
For general purpose computer, it loads the operating system (Windows, iOS, Android, etc.) from hard drive or Flash memory to the RAM
For Arduino Uno, it does the following
  Check for new programming command from IDE
  If yes, start to download new programme from PC
  If no, load latest programme stored in the Flash memory
The Arduino Uno Bootloader program is activated upon power up or reset

## Slide 31: SUMMARY
Arduino Uno MCU Board
  ATMega 328 MCU
    Number of bits, processor speed
    Memory: RAM, EEPROM, Flash Memory
  Other components
    Digital I/O pins, ADC pins, power supply
  Programming Environment: Arduino IDE
  Connecting PC to Arduino Board
  Bootloader Program