## Slide 1
MA2012 INTRODUCTION TO MECHATRONICS SYSTEMS DESIGN
Lecture 3
Prof Ang Wei Tech
College of Engineering
School of Mechanical and Aerospace Engineering

## Slide 2: RECAP
Arduino Uno MCU Board
  ATMega 328 MCU
    Number of bits, processor speed
    Memory: RAM, EEPROM, Flash Memory
  Other components
    Digital I/O pins, ADC pins, power supply
  Programming Environment: Arduino IDE
  Connecting PC to Arduino Board
  Bootloader Program

## Slide 3: MECHATRONIC SYSTEM COMPONENTS

## Slide 4: SENSOR
Transducer
  A device which converts one form of energy into another
Sensor
  A transducer which performs measurement
  A device which produces an output signal (typically electrical) for the purpose of sensing a physical phenomena

## Slide 5: SENSORS: ANALOG VS DIGITAL
Analog
  Sensed quantity (voltage, current, etc.) is continuous
  Usually (not always) needs an Analog to Digital Converter (ADC) to interface with MCU
Digital
  Sensed quantity is discrete
  Two-state devices: e.g. switches, Proximity Sensors
    ON / OFF, High(1) / Low(0)
  Multiple-state devices
    Encoder: incremental and absolute

## Slide 6: DIGITAL SENSORS
Switches
Single Pole, Throw
Single
Double
Toggle Switch
Slotted Opto Switch

## Slide 7: DIGITAL SENSORS
Switches
Limit Switch
NC
NO
Common

## Slide 8: DIGITAL SENSORS
To detect presence of an object
  Output: High or Low upon detection
Working principles
  Infrared, Ultrasound: detection of incident waves reflected by object
    E.g. Car reverse sensor
  Inductive: change of induced current upon detection of ferrous materials
    E.g. Metal detectors for security
  Capacitive: change of capacitance upon detection of conductive materials
    E.g. Touch screen
Infrared proximity sensor
Inductive / Capacitive proximity sensor
Proximity sensor

## Slide 9: DIGITAL SENSORS
Digital Encoders
Optical
Hall-Effect
Rotary
Linear

## Slide 10: DIGITAL SENSORS
Incremental Encoder
  Same working principle as
  opto switch
  ChA leads ChB by 90: CCW
  ChA lags ChB by 90: CW
  ChZ is a Home (Ref) pulse
  Time (Ti) between 2 pulses
  determines the rotation speed:
  i = 2 / Ti
Absolute Encoder
  To be taught in other course
Z
  Ti

## Slide 11: INTERFACING WITH DIGITAL SENSORS
Sensing modalities
  To sense a State: HIGH or LOW
  To measure the time duration of a State
Communication Protocols
  Serial – one data after another
    Synchronous vs Asynchronous
    Cheaper but slower
  Parallel – multiple data via multiple I/O pins
    More expensive but faster

## Slide 12: ANALOG SENSORS
POTENTIOMETER
To measure angular or linear displacement
Working principle: Voltage divider
  Variable resistance  Variable voltage
Applications
  Light dimmer
  Audio volume knob
W
A
B
To MCU via ADC

## Slide 13: ANALOG SENSORS
ACCELEROMETER
To measure linear acceleration (movement & gravity)
  Output: Voltage (Analog) or Duty Cycle (Digital)
Working principle:
  Motion causes change of distance between plates and hence change of capacitance
Applications
  Mobile device
  Inclinometer

## Slide 14: ANALOG SENSORS: DATA ACQUISITION
The process of sensing a physical state and convert it into digital form for processing, presentation and storage
Elements of Data Acquisition (DAQ) process:

## Slide 15: ELEMENTS OF DATA ACQUISITION PROCESS
Sensing Element
  This is in contact with the process and gives an output which depends in some ways on the variable(s) to be measured
  E.g.
    Thermocouple: mV e.m.f depends on temperature
    Strain gauge: resistance depends on mechanical strain

## Slide 16: ELEMENTS OF DATA ACQUISITION PROCESS
Signal Conditioning Element
  This takes the output of the sensing element & converts it into a form more suitable for further processing, usually a d.c. voltage, d.c. current or frequency signal
  E.g.
    Amplifier which amplifies mV to V
    Wheatstone bridge that converts impedance change into voltage change

## Slide 17: ELEMENTS OF DATA ACQUISITION PROCESS
Signal Processing Element
  This takes the output of the signal conditioning element and converts it into a form more suitable for presentation
E.g.
  ADC which converts a voltage into a digital form
  Computer which calculates the desirable measurement from raw data
    Mass of gas from flow rate and density
    Correction for non-linearity

## Slide 18: ELEMENTS OF DATA ACQUISITION PROCESS
Data Presentation Element
  This presents the measured value in a form which can be easily recognized by the observer
E.g.
  Visual Display Unit (VDU)
  Dial or pointer-scale indicator

## Slide 19: EXAMPLES OF DAQ PROCESS

## Slide 20: DIGITIZATION OF ANALOG SIGNAL
Higher Sampling Rate & Resolution
Digitized signal is a series of numbers which approximates an analog signal at the sampling time instances
Two important parameters
  Sampling rate (x-axis)
  Digitization resolution (y-axis)

## Slide 21: SHANNON SAMPLING THEOREM
No maximum sampling frequency
  Higher frequency also means more noise, higher cost
Sampling frequency (fs) must be at least 2 times higher than the highest frequency component (fmax) in the signal
fs > 2fmax ; Ts < 0.5Tmin [Period T = 1/f ]
  Nyquist frequency = 2fmax
Consider the following 1 Hz signals:
fs = 1.33 Hz
Ts = 0.75 s
2 samples
Ok!
fs = 1.33 Hz
Ts = 0.75 s
Only 1 sample
NOT ok!
fs = 2.0 Hz
Ts = 0.5 s
Both samples measure 0.
NOT ok!
fs > 2.0 Hz
Ts < 0.5 s
At least 2 non-zero samples.
Ok!

## Slide 22: ALIASING
An effect that causes different signals to become indistinguishable (or aliases of one another) as a result of under-sampling
  E.g. Original signal 10 cycles at f0
  fs = 1.2 f0
  Total 12 sampling points
  Sampled signal
  appears to be 0.2 f0

## Slide 23: ALIASING - EXAMPLE
Wheels of forward moving car appear to rotate backward!
Click video to play

## Slide 24: ANALOG-TO-DIGITAL CONVERSION
Quantizing Theory
  Quantizing – conversion of continuous analog signal to a series of discrete states
  Coding – assignment of a digital code number to each state
Number of states, N = 2n
states: 0 … N–1
n–number of bits of A/D conversion

## Slide 25: ANALOG-TO-DIGITAL CONVERTER
Successive Approximation
  Fast, cheap, most widely used
  A/D Conversion Steps
    With a start signal, analog input is temporarily stored at the sample & hold (S&H) latch
    The control unit makes an approximation of an digital equivalent of the analog input and hold the result at an output latch
    The D/A converts the digital approximation to an analog signal and compares it with the analog input
    If both equal, result held at the latch is output.
    If not equal, go back to Step 2 to make the next successive approximation iteration.

## Slide 26: ANALOG-TO-DIGITAL CONVERTER
Successive Approximation E.g.
  Full Scale (FS) = 1.0 V
  Resolution (n) = 4 bits
  Analog Input = 0.4 V
  Control unit turns on only the most significant bit (MSB) Bit 3 which represents ½ FS = 0.5V. 1st approximation = 1000
  It is larger than Analog Input (0.4V), hence Bit 3 is turned off.
  Control unit turns on Bit 2 (1/4 FS = 0.25V). 2nd approximation = 0100
  Current value (0.25V) < 0.4V, hence Bit 2 is remained on.
  Control unit turns on Bit 1 (1/8 FS = 0.125V). 3rd approximation = 0110
  Current value (0.25 + 0.125 = 0.375V) < 0.4V. Bit 1 is remained on.
  Control unit turns on Bit 0 (1/16 FS = 0.0625V). 4th approx = 0111
  Current value (0.375 + 0.0625 = 0.4375V) > 0.4V. Bit 0 is turned off.
  Final output = 0110 = 0.375V

## Slide 27: ANALOG-TO-DIGITAL CONVERTER
Flash Converter
  Fastest type
  Increasing resolution does not increase conversion time
  A series of comparators acting in parallel to approximate an analog input
  Flip-flop latches produce 3-bit code
  AND & OR gates to convert 3-bit code to Binary output

## Slide 28: ANALOG-TO-DIGITAL CONVERTER
Flash Converter
State | Code (G2G1G0) | Binary (B1B0) | Voltage Range (V)
0 | 000 | 00 | 0 – 1
1 | 001 | 01 | 1 – 2
2 | 011 | 10 | 2 – 3
3 | 111 | 11 | 3 – 4

## Slide 29: SUMMARY
Digital Sensors
  Switches, Incremental Encoder
  Interfacing with Digital Sensors
ANALOG SENSORS
  Analog Output (e.g. Potentiometer), Digital and Analog Outputs (e.g. accelerometer)
Acquisition process and elements
Digitization of analog signal
  Shannon sampling theorem, Nyquisit frequency, Aliasing
A/D Conversion, ADC
  Successive Approximation
  Flash Converter