## Slide 1
MA2012
C++ Programming for Arduino
Outline:
Introduction to C++ & Arduino IDE
Variable and Datatype
Control Statements
Operations
Functions
Class
Others

## Slide 2
Introduction to C++ & Arduino
C++
A general-purpose programming language, cross-platform, compatible with C
Object-oriented with well encapsulated class
Close to hardware, and maintains some degree of access to low-level programming functions (memory management, etc.)

## Slide 3
Introduction to C++ & Arduino IDE
Arduino IDE
A text editor
Supports C++ programming language
Uploads the program to the controller
Allows communication between the controller and the PC
Serial Monitor:
a debugging and communication tool

## Slide 4
Introduction to C++ & Arduino IDE
Hello-world C++ program
Comment multiple lines. In Python: ’’’……’’’
Comment single line.
In Python: #......
Include some standard libraries
Namespace avoids name collisions
main function. It can also have parameters like:
int main (int argc, char *argv[]){}. main() function is the entry point to the program
Return value
Display the output to the monitor
Insert newline

## Slide 5
Introduction to C++ & Arduino IDE
Program structure in Arduino
setup(): The function is to initialize variables, pin modes, start using libraries, etc. The setup() function will only run once, after each powerup or reset of the Arduino board.
loop(): This function does precisely what its name suggests, and loops consecutively, allowing your program to change and respond.
https://www.arduino.cc/en/Tutorial/BuiltInExamples/BareMinimum/
Why there is no main() function?

## Slide 6
Introduction to C++ & Arduino IDE
Comparison between C++ & Python
C++ | Python
No garbage collection | Has inbuilt garbage collection
Compiler (will be compiled once to generate the executable file) | Interpreter (statement by statement)
Suitable for Application and system programming, games, computer graphics, mechatronics, and etc. | Wildly used in Web development, data analysis, AI, etc.
Efficient, fast and stable | Extensive support library but lower running speed

## Slide 7
Variables and Data types in C++
Common used data types in C++
Declaration |  |  | Bytes (Uno)
Signed | Unsigned |  | 
[signed] char | unsigned char |  | 1
short | unsigned short |  | 2
int | unsigned |  | 2
long | unsigned long |  | 4
char * |  |  | 2
float |  |  | 4
double |  |  | 4
Some other data types: bool, void, array and etc.
One byte = collection of 8 bits
int : range from -32768(-2^15 ) ~ 32767 (2^15 -1)
unsigned int: range from ? to ?
int buttonPin = 4;
const int Pin1 = 3; // keyword const indicates that Pin1 // is a read-only value, cannot be changed
bool pinPressed = false;
float a = 3.14;
double b = 6.22;
Notes: Why these is no unsigned float? Precision vs Range

## Slide 8
Variables and Data types in C++
Variable are containers for storing data values, they must be declared before use (different from the usage in Python)
int pinNumber = 10; //single variable
int pinNum1, pinNum2, pinNum3; // multiple variables
C++ is a strongly typed language (Python is weakly typed)
int n = 10; // int type variable
n = 100;
n = “https://www.ntu.edu.sg/Pages/home.aspx” // string cannot be assigned to an int //variable
url = “https://www.ntu.edu.sg/Pages/home.aspx” // unspecified type
Data type
Variable name
initialization
C++ is case sensitive

## Slide 9
Variables and Data types in C++
Comparison between C++ & Python
C++ | Python
int a = 0; // declared with type | a = 0; // datatype is set when a // value is assigned to a variable
int n = 10; n = ‘a’; //Error, not allowed | n = 10 # integer n = “Hello” # string
int a = 0, b= 0, c=0; | a = b = c = 0
Notes: Why these is no unsigned float? Precision vs Range

## Slide 10
Variables and Data types in C++
Array
A collection of homogeneous data (data of the same type)
int ages [5]; // declaration of an array with 5 elements of type int
int ages [5] = {16, 17, 18, 15, 17}; // explicitly initialize the array in declaration
int ages[] = {16, 17, 18, 15, 17}; // declaration without specified limits
16 | 17 | 18 | 15 | 17
ages
0 | 1 | 2 | 3 | 4
Array index starts from zero
bool female[5] = {0, true, false, -200}
female[5] = true; // store value into last, 5th element
Array is not assignable
bool male [5];
male = female; //

## Slide 11
Variables and Data types in C++
Array(Two dimensional)
Declaration & Initialization
int seatID [2][3]; // declaration of 2D array with 5 rows and 8 columns
int seatID[2][3] = {{1, 2, 4}, {3, 5, 6}}; 1️⃣
int seatID[2][3] = {1, 2, 3, 4, 5, 6}; 2️⃣
int seatID[2][3] = {{1, 2}, 4}; 3️⃣
int seatID[][3] = {1, 2, 3, 4, 5, 6}; // how about seatID[][3] = {1, 2, 3, 4, 5, 6, 7}
1 | 2 | 3
4 | 5 | 6
1 | 2 | 0
4 | 0 | 0
1 | 2 | 3
4 | 5 | 6
7 | 0 | 0
1 | 2 | 4
3 | 5 | 6
1️⃣
2️⃣
3️⃣
Second subscript
first subscript

## Slide 12
Variables and Data types in C++
Data type - pointer
A pointer is a variable that stores the memory address as its value
int x, y;
int *ptr1; // pointer variable, which points to an integer data
// “*”, Pointer operator, declare a pointer
int **ptr2; // pointer points to a pointer
ptr1 = &x; // get the address of x, and stores it in ptr1.
//“&” Pointer operator, get the address of the variable
*ptr1 = 300; // assign 300 to the address stored in ptr1.
//“*”, dereference a pointer
ptr2 = &ptr1; // put the address of ptr1 in the place with the // address of ptr2
300
0x1001
0x1003
variable
name
content
address
0x1001
0x1002
0x1003
0x1004
…
…
x
y
ptr1
ptr2

## Slide 13
Variables and Data types in C++
Data type - void
The void keyword is used only in function declarations. It indicates that the function is expected to return no information to the function from which it was called.

## Slide 14
Variables and Data types in C++
Scope of variables in C++
When a variable is declared, it can only be ”seen” and used in certain part of the program
Typically, there are two types of variable scopes
  Local variables
  Global variables
int myID = 123; // global variable
void setup() {
int hisID = 321; // local variable in setup()
}
void loop() {
Serial.println(myID); // serial monitor will display myID
Serial.println(hisID); //
int myID = 101; // local variable, same name as the global variable myID
Serial.println(myID); // What number will be displayed in serial monitor?
}

## Slide 15
Control Statements
Selection Statements
if (a > b) {
// do thing A...
} else {
// do thing B...
}
switch (a) {
case 1:
// do something when a = 1 ...
break;
case 2:
// do something when a = 2 ...
break;
default: // optional
}
if – else statement
Valid conditions:
  Comparison
  Integer values (0 = false, others = true)
switch-case statement
Variables(var) in switch() must be integer (or can be converted to integer)
break: stop and exit switch()
default: catch all unmatched cases

## Slide 16
Control Statements
Repetition Statements
while (a > b) {
// do something…
}
for (A; B; C) {
// do something…
}
while statement
Valid conditions:
  Comparison
  Integer values (0 = false, others = true)
  Checking condition can be before or after executing the body
for loop
Statement A: initialization (eg. int i = 0). Will be executed only once before the execution of the code block
Statement B: condition (eg. i < 100). Define the condition of the code block
Statement C: update (eg. i++). Will be executed every time after the code block has been executed
do {
// do something…
} while (a > b)
while a > b:
# do something…
In python

## Slide 17
Control Statements
for loop in C++ and Python
for (int i = 1; i<7; i++){
cout<<i<<endl;
}
for x in range(1, 7):
print(x)
if-else in C++ and Python
if (i>2){
cout<<i<<endl;
} else {
cout<<-i<<endl;
}
if (i>2):
print(x)
else:
print(-i)

## Slide 18
Operations
Operator | Description | Example | Result (a)
= | assignment | int a = 2 | 2
+ | addition | int a = 3+2 | 5
- | subtraction | int a = 3-2 | 1
* | multiplication | int a = 3*2 | 6
/ | division | double a = 3/2 | 1.5*
% | modulo | int a = 3%2 | 1
* int a = 2; int b = 3; double c; c = b/a; What is the value of c?
Arithmetic operators
Unlike Python, there is no exponent operator in C++. It can be realized with the function:
pow (x, y); //

## Slide 19
Operations
Expression | Equivalent to…
y += x | y = y + x
y -= x | y = y - x
y /= x | y = y / x
y *= x | y = y * x
Compound assignment
Increment and decrement
 | Equivalent to…
++x or x++ | x = x + 1
--x or x-- | x = x - 1
Any difference between ++x and x++?
int x = 5;
int y, z;
y = x++; // y = 5, x = 6
z = ++x; // z = 7, x = 7
Notes: In expressions, ++x do the self increment first, then return the value of x; x++ firstly return the value of x, then do the self increment.

## Slide 20
Operations
Operator | Description
== | Equal to
!= | Not equal to
< | less than
> | larger than
>= | No smaller than
<= | No larger than
Relational and comparison operators
Operator | Example | result
! (not) | !(5 == 6) | true
&& (and) | (5 == 5) && (4 <5) | false
¦¦ (or) | (5 == 5) ¦¦ (4 <5) | true
Logical operators
In Python, the operators are not, and, or.

## Slide 21
Operations
Explicit type casting operator
It allows to convert a value of a given type to another type
float y = 3.14;
int x = (int) y; // x = 3
int a = 2; int b = 3; double c; c = b/a; What is the value of c?
Recall
How to get the accurate value?
int a = 2;
int b = 3;
double c;
c = (double) b/a; // c = 1.5
y = 3.14
x = int(y); # x = 3
Casting in Python
Notes: is to precede the expression to be converted by the new type enclosed between parentheses (()):

## Slide 22
Operations
Representation of Numbers
Decimal number:
Binary representation:
Hexadecimal:
19
2
9
2
4
2
2
2
1
2
0
1
0
0
1
1

## Slide 23
Operations
Bit-level operation
  Boolean operations
~ | 
0 | 1
1 | 0
& | 0 | 1
0 | 0 | 0
1 | 0 | 1
¦ | 0 | 1
0 | 0 | 1
1 | 1 | 1
^ | 0 | 1
0 | 0 | 1
1 | 1 | 0
NOT
AND
OR
EXCLUSIVE OR
~ | 
 | 1100
 | 0011
& | 0110
 | 1100
 | 0100
¦ | 0110
 | 1100
 | 1110
^ | 0110
 | 1100
 | 1010

## Slide 24
Operations
Bit-level operation
  Shift Operations
  << or >>, for shifting bit patterns to the left or to the right
For an operand x having bit representation []
Left shift: the expression x<<k yields a value with bit representation [], which means that x is shifted k bits to the left, dropping off the k most significant bits and filling the right end with k zeros
Right shift:
Logical: correspondingly, x>>k will shift x to the right with k bits. The left ends will be filled with k zeros. []
Arithmetic : The left ends will be filled with k repetitions of the most significant bit
Value of X | [01100011] | [10010101]
x<<4 | [00110000] | [01010000]
x>>4 (logical) | [00000110] | [00001001]
x>>4 (arithmetic) | [00000110] | [11111001]

## Slide 25
Function
A function is a subprogram that returns a single value. You must declare and define a function before invoking it. You can either declare and define it at the same time, or you can declare it first and then define it later in the same block. Codes after the return statement will not be executed.
Self contained
  only relies on input parameter
  output is well defined
Portable
Ease of maintenance

## Slide 26
Function
Declaration:
duration_off
Definition:
duration_off
Call the functions, pass by value
Definition:
duration_on

## Slide 27
Function
functions in C++ and Python
sayGoodBye is defined before it is called
sayHello is declared before it is called
sayHello is defined after it is called
C++
Python
Function must be defined before it is called
Nested function. Not supported in C++
Unless it is called by another function

## Slide 28
Class in C++
C++ is an object-oriented programming language.
Everything in C++ is associated with classes and objects, along with its attributes and methods. For example: in real life, a car is an object. The car has attributes, such as weight and color, and methods, such as drive and brake.
Attributes and methods are basically variables and functions that belongs to the class. These are often referred to as "class members".
A class is a user-defined data type that we can use in our program, and it works as an object constructor, or a "blueprint" for creating objects.

## Slide 29
Class
A Button class object (Button1) is created.
The button and the LED are connected to pin 13 and 6, respectively.
Open the serial monitor, if the button is pressed, there will be a sentence “State is High”. Otherwise, there will be ”State is Low”.
Then the destructor function will let the serial monitor display “Bye Bye”

## Slide 30
Macros
A macro is a fragment of code which has been given a name. Whenever the name is used, it is replaced by the contents of the macro. There are two kinds of macros. They differ mostly in what they look like when they are used. Object-like macros resemble data objects when used, function-like macros resemble function calls.

## Slide 31
Header file
# include " q-char-sequence " new-line:
search the files under the same directory of the source file
# include < h-char-sequence > new-line:
search the files under the specified directory or the default directory where standard library files locate
It is recommended to put your own header file and other .cpp files under the same directory of your main file. Otherwise, you need to specify the route when you compile the code

## Slide 32
Header file
Functions are declared in the header file
Functions are implemented in another .cpp file

## Slide 33
Header file
https://www.learncpp.com/cpp-tutorial/header-guards/
Header Guards
Header guards help to avoid the duplicate definition problem

## Slide 34
Header file
Practice in Python
helloworld.py and hello.py are in the same folder