## Slide 1: MA2012 Introduction to Mechatronics Systems Design (Lecture 8)
A/P Ang Wei Tech
  Email: wtang@ntu.edu.sg
  Tel: 6790-4911
  Office: N3.2-01-04
CA Result
  Class mean = A+

## Slide 2: Lecture 1 – Introduction 
Mechatronics System Components & Examples: Car, Printer, etc.

## Slide 3: Lecture 2 – Arduino UNO MCU 
  ATMega 328 MCU
      Number of bits, processor speed
      Memory: RAM, EEPROM, Flash Memory
      Memory allocation in different application scenarios
  Other components
      Digital I/O pins, ADC pins, power supply
  Programming Environment: Arduino IDE
  Connecting PC to Arduino Board
  Bootloader Program

## Slide 4: Lecture 3 – Sensors     
Digital Sensors
  Switches, Incremental Encoder
  Interfacing with Digital Sensors
Analog Sensors
  Digital Output (e.g. Proximity sensor), Analog Output (e.g. Potentiometer), Digital and Analog Outputs (e.g. accelerometer)
Acquisition process and elements

## Slide 5: Lecture 3 – Sensors     
Digitization of analog signal
  Shannon sampling theorem, Nyquisit frequency, Aliasing
A/D Conversion, ADC
  Successive Approximation, Flash Converter
  Interfacing with ADC

## Slide 6: Lecture 4 – Actuators     
Direct Current (DC) Motor
      Construction
        Brushed vs Brushless
      Control
        Pulse Width Modulation (PWM)
        Inductive Kickback & Diode protection
    Servomotor
  Working principle
  Control: Mark length

## Slide 7: Lecture 4 – Actuators     
Solenoid
      Construction & Control
    Stepper Motor
      Construction & Working Principle
        Unipolar – 2 windings per phase, one for each direction of magnetic field
        Bipolar – 1 winding per phase, needs a H-Bridge circuit to change direction
      Control
    Wave Drive / Single Phase
    Two Phase Full Step
    Two Phase Half Step
    Microstepping

## Slide 8: Lecture 5 – Signal Conditioning    
Signals & Noise
  Deterministic vs random signals
  Noise characteristics & sources
  Signal-to-Noise Ratio
Input Signal Conditioning
  Deflection Bridge: Quarter, Half, Full
  Op-amps: Inverting, non-inverting, differential, voltage follower, voltage adder
  Filters: Low Pass, High Pass
  Averaging
Output Signal Conditioning
  Digital-to-Analog Converter

## Slide 9: Lecture 6 – Communications 
Interfacing with I/O devices
  MCU-Initiated
    Unconditional transfer, no handshaking
    Conditional transfer (Polling), handshaking is required
  Device-Initiated
    Interrupt transfer, handshaking is required
    Characteristics of Interrupt Service Routine (ISR)
    Hardware interrupt in Arduino
  Polling vs Interrupting

## Slide 10: Lecture 6 – Communications     
Parallel vs Serial Communications
Universal Asynchronous Receiver Transmitter (UART)
Data transmission rate
Synchronous vs Asynchronous communications
I2C Bus and SPI Bus
  Characteristics, Communication protocols
  Advantages
Wireless communications
  Bluetooth
  WIFI

## Slide 11: Lecture 7 – Mechatronics Systems     
Understand the task, define the problem
Sketch a functional block diagram
Decide & select mechatronics components (type, number, communication protocol, etc.) :
  Digital control architecture
  Sensors & input interfacing
  Actuators & output interfacing
  Display
Construct hardware prototype
Programme software / firmware

## Slide 12: Examination
Date/Time/Venue: 07 Dec / 1:00 PM / Hall A
Format:
  2h
  Closed book
  4 questions
  Answer all
50% of Final Grade

## Slide 13: Exam Scope & Question Types
Short questions on sensors, actuators, I/O devices and interfacing
  Given a problem/task/scenario, identify suitable component(s) or techniques and explain choice
Circuit & Programming
  Given a circuit, write sub-routines to fulfill certain task requirements.
  Given a sub-routine, interpret what the codes are trying to do

## Slide 14: Exam Scope & Question Types
Design of mechatronics systems with Arduino UNO MCU
  Given a problem/task/scenario, design a mechatronics system: description and/or block diagrams
Interfacing Arduino UNO MCU with sensors and/or actuators
  Given a datasheet(s) of sensor and/or actuator, answer short questions, sketch simple circuits, do simple calculations, write C++ codes, etc.

## Slide 15: Exercise 1
You are to design a control system of a spinning lucky draw wheel at an amusement park.
When a participant presses a button, the wheel will spin at around 30 rpm; when the button is released, the wheel is allowed to spin freely until it stops.
There are 16 different prizes to be won. Your system has to automatically identify the sector at the 12 o’clock position and display the associated prize on a dot matrix display.

## Slide 16: Exercise 1
Sketch a schematic block diagram to show your design of the control system for this application.
Indicate and describe clearly in your diagram all the required mechatronic components (Arduino UNO MCU, sensors, actuators, I/O devices, interfacing devices, power sources, etc.) and their relationships. You may assume the system uses a 12VDC battery pack.
Your answer need to specify only the component type, information on the make and model of components are not necessary

## Slide 17: Exercise 1
Arduino UNO MCU
7V
DC Motor Driver
12V
DC Motor spinning wheel
Encoder
5V
5V / 7V regulator
12V
5V / 7V
Power Indicator LED
5V
Push Button

## Slide 18: Exercise 2
You are to design an automatic temperature control system to keep a car warm.
There are two control settings: temperature & fan speed. Both settings has 3 levels of control: Low, Medium, High.
In the manual mode, you may independently set the level of temperature and fan speed.
In the automatic mode, you set the
level of temperature (L-M-H) and the
computer will adjust the heating coil
temperature & fan speed to reach and
maintain it within the desired
temperature range

## Slide 19: Exercise 2
Sketch a schematic block diagram to show your design of the control system for this application.
Indicate and describe clearly in your diagram all the required mechatronic components (Arduino UNO MCU, sensors, actuators, I/O devices, interfacing devices, power sources, etc.) and their relationships. You may assume the car runs with a 24VDC battery.
Your answer need to specify only the component type, information on the make and model of components are not necessary

## Slide 20: Exercise 2
Temp Sensor #1
5V
5V / 7V regulator
24V
5V / 7V
Power Indicator LED
Temp Sensor #2
5V
DC Motor Driver
24V
DC Fan Motor
Arduino UNO MCU
7V
Heat coil driver
24V
Heat Coil
Temperature Dial (pot)
5V
Fan Speed Dial (pot)
5V

## Slide 21: Exercise 3
The application described in Ex. 2 requires 2 temperature sensors to be mounted in the car, one near the driver’s seat and the other one near the back row seat. Given the datasheet of Analog Devices TMP3x Low Voltage temperature sensor. Answer the following questions:

## Slide 22: Exercise 3
Describe how can we use the SHUTDOWN function to minimize the power consumed by the temperature sensor when the car engine is off.
  MCU sends a Logic 0 (LOW) to the SHUTDOWN pin
Which packaging type (SOT-23/SOIC_N/TO-92) should we choose?
  SOIC_N or SOT-23. (See Datasheet pg 9, section Shutdown Operation)

## Slide 23: Exercise 3
  How would you interface this sensor with an Arduino UNO MCU? Describe in words and sketch a schematic diagram.
  The temperature sensor Vout pin is connected to one of the Analog Input pins of Arduino UNO MCU
  The Shutdown pin is connected to a Digital I/O pin.
Temp Sensor
Vout
Shutdown
5V
Arduino UNO MCU
A0
D0
7V

## Slide 24: Exercise 3
If the car is designed for all weather conditions, i.e. –30 to +45C, which model (35/36/37) should we choose? Why?
  All models can be used but TMP36 should be chosen because the scale factor is rated in this temperature range, i.e. performance can be guaranteed.
If the car is designed for sub-tropical conditions, i.e. +5 to +30C, and it is desirable to maximize the sensitivity, which model should we choose? Why?
  TMP37. Because it is the most sensitive (20 mv/deg).

## Slide 25: Exercise 4
The game in Ex.1 is changed such that only 1 out of 16 sectors will win the grand prize, and all others win nothing. The design of the system is such that a sensor senses no object (slit) when a prize is won.
Given the datasheet of Omron proximity sensor E2EM. Answer the following questions:
Sensor
Slit (12x50mm)
Al Strip (2.5 mm thickness)

## Slide 26: Exercise 4
If the distance between the sensor and the rim of the wheel is 10mm, which model should you use?
  E2EM-X30MX. Refer to pg 4 bottom right graph, see plot for Aluminum.
If it is required to send a LOW to a MCU when the slit is detected, should you choose NC or NO type?
  NO. Because when the slit (i.e. no object) is detected, the output is LOW.
Discuss the trade-off of selecting shielded vs unshielded model.
  Unshielded: longer sensing distance but more noise
  Shielded: vice versa

## Slide 27: AY16/17 Q2
A mechatronics engineer implemented a measurement system using an Arduino UNO MCU. The measurement system has a digital temperature sensor and an analog accelerometer to monitor the conditions of a piece of equipment. The temperature sensor records the ambient temperature of at a sampling frequency of 10 Hz. A 4-digit Liquid Crystal Display (LCD) is used to show real-time measurement of the temperature (see Figure 1) with 2 decimal points. The accelerometer is used to measure the vibration of the equipment caused by movement activities in its vicinity and is sampled at 200 Hz.

## Slide 28: AY16/17 Q2
An operator observes that the least significant digit of the LCD is fluctuating all the time while the ambient temperature is held constant. Explain the cause of this observation. (2 mark)
This fluctuation is caused by random or white noise.
The temperature sensor has a resolution of 12-bit and the sensing range is from 10 – 90C. The fluctuation is only in the range of  1 bit from the true temperature. Given that the true temperature is 30.00C, what are the 3 possible temperatures which the display will show? (9 marks)
12 bit is equivalent to 212 = 4096 levels
Temperature range = 90 – 10 = 80C
Resolution = 80 / 4,096 = 0.02C
The 3 possible temperatures to be displayed are 29.98, 30.00 & 30.02.

## Slide 29: AY16/17 Q2
Suggest 3 possible ways to make the temperature reading shown on the LCD to stop fluctuating so frequently. (6 marks)
Any 3 of the following:
  Use a lowpass filter
  Perform a moving average
  Display only 1 decimal point
  Update display every minute (or any time period significantly longer than sampling period)
An analysis of a short period of recording by the accelerometer reveals that the signal is made up of a 1 Hz signal caused by a person walking pass the equipment, a 50 Hz noise caused by powerline hum, and random noise. Suggest how this powerline hum can be removed without affecting the 1 Hz signal. (3 marks)
To use a lowpass filter with a cut-off frequency between 10-40 Hz.
Or to use a bandstop filter centered at 50Hz.

## Slide 30: AY16/17 Q2
Why is the powerline hum not observed in the temperature sensor recording? (3 marks)
Because the sampling frequency is lower than the Nyquist frequency to sense the 50 Hz powerline hum.
If a digital accelerometer is used instead of an analog one, would the powerline hum be still unobservable? (2 marks)
Yes

## Slide 31: AY19/20 Q2
Name two advantages and two disadvantages of DC motors as compared with Stepper motors.
(4 marks)
Advantages of DC Motor vs Stepper Motor (any 2):
Easier to control in velocity control mode
Possible to control in torque control mode
Cheaper to implement in velocity control applications
Higher torque in high speed applications
Disadvantages (any 2):
Harder to control in displacement/position control mode
Lower holding torque in positioning applications
Lower torque at low speed applications
More expensive to implement in positioning applications

## Slide 32: AY19/20 Q2
In general, a DC motor may be controlled in speed control mode or torque control mode. Explain how you can use an Arduino UNO MCU only (i.e. without a peripheral driver) to control a DC motor in these two control modes.
(4 marks)
Speed control mode: Not possible, need a driver
Torque control mode: not possible with Arduino UNO

## Slide 33: AY19/20 Q2
When controlling a DC motor, it is mandatory to add a flyback diode in the circuit, as illustrated in Figure 2. Explain why this is necessary.
(4 marks)
The steady-state current though an inductor, cannot immediately go to zero when the switch (physical or transistor) is opened. The changing current induces a voltage across the inductor, making the potential of the ground end of the inductor greater than the Vcc end, and will cause the switch to ‘blow up’. Kickback or flyback diode protects the switch from blowing up.

## Slide 34: AY19/20 Q2
There are several ways to control a unipolar Stepper motor. State one advantage of each of the three popular control methods: Wave Drive, Two Phase Full Step and Two Phase Half Step.
(3 marks)
Wave Drive: Simplest to control
Two Phase Full Step: Highest holding torque
Two Phase Half Step: Highest positioning resolution/accuracy

## Slide 35: AY19/20 Q3
A geologist wishes to map the profile of a cave with a river running through it. As illustrated in Figure 5, his idea is to use a remote control boat to go upstream, carrying a laser scanning device.
The laser scanning device is made up of an Arduino UNO MCU, a Flash memory module, a pair of laser range sensors, each attached to a tilt motor which has a range of 135 degrees.
The boat is equipped with a battery powered power-supply (also provide power to the laser scanning device), a rudder steering motor, a motor with propeller, an ultrasonic speed sensor to measure the boat speed, an Arduino UNO MCU and a wireless communication module.
The remote controller consists of an Arduino UNO MCU, a wireless communication module, a battery and two potentiometers for speed and steering control.
Sketch a schematic block diagram to show your design of the control systems for this application. Indicate and describe clearly in your diagram all the mechatronic components (Arduino UNO MCU, sensors, actuators, I/O devices, interfacing devices, power sources, etc.) and their relationships to each other. You may make appropriate assumptions to add new components (e.g. switches), but you need to state them clearly.
Your answer need to specify only the component type. Information on the make and model of components are not necessary.
(25 marks)

## Slide 36: AY19/20 Q3

## Slide 37: Homework
AY1516 Q4
AY1617 Q4
AY1718 Q2
AY1920 Q4
AY2021 Q4
AY2122 Q3
AY2223 Q4
Solutions shall be posted on 30 Nov
Good Luck!