## Slide 1
MA2012 INTRODUCTION TO MECHATRONICS SYSTEMS DESIGN
Lecture 5
Prof Ang Wei Tech
College of Engineering
School of Mechanical and Aerospace Engineering

## Slide 2: Mechatronic System Components
MECHANICAL SYSTEM
-system model -dynamic response
ACTUATORS
-solenoid, voice coils
-DC motors
-stepper motors
-servo motors
-hydraulics, pneumatics
SENSORS
-switches -strain gage
-potentiometer -thermocouple
-photoelectrics -accelerometer
-digital encoder -MEMs
INPUT SIGNAL
CONDITIONING
AND INTERFACING
-discrete circuits -filters
-amplifiers -A/D, D/D
GRAPHICAL
DISPLAYS
-LEDs -LCD
-digital displays -CRT
OUTPUT SIGNAL
CONDITIONING
AND INTERFACING
-D/A, D/D -power transistors
-amplifiers -power op amps
-PWM
DIGITAL CONTROL
ARCHITECTURES
-logic circuits -sequencing and timing
-microcontroller -logic and arithmetic
-SBC -control algorithms
-PLC -communication

## Slide 3: Process/ Instrument Control I/O
MCU operates automatically and continuously under the control of the program stored in ROM, no human intervention
  Operation is changed only by changing the content of the ROM
During execution, MCU receives data from devices monitoring some physical states (temperature, speed, etc.), operates on the data and sends data or control signals to the process/ instrument via output devices
E.g. Traffic red-light camera, car air-bag system, fire/ burglar alarm system, etc.

## Slide 4: Keyboard Entry/Display I/O
Communications with human operators
MCU executes a keyboard monitoring program stored in ROM
  Reads the keyboard continuously until a key is actuated, determines the actuated key, and executes the appropriate instructions
Once the instructions are executed, it gets back to keyboard monitoring program
E.g. Point-of-sale machine, lift, television, etc.

## Slide 5: Input / Output Interfacing
I/O Interfacing Modes
MCU Initiated
Unconditional Transfer
Conditional Transfer
Device Initiated
Interrupt Transfer

## Slide 6: MCU-Initiated Transfer
Unconditional transfer
  I/O device must always be ready for communication
  Examples
    To input a 8-bit data word from a set of 8 switches
    Output data to LEDs
MCU-initiated transfer

## Slide 7: MCU-Initiated Transfer
Conditional transfer
  Communication takes place only when the I/O device is ready
  Handshaking
    MCU send a data available (DAV) control signal to an output device
MCU
Interface Circuit
Output Device
DAV
DACK
Data
Data
    Upon receiving the DAV signal, the output device accepts the data, then send a data accepted (DACK) control signal back to the MCU
MCU-initiated transfer - handshaking

## Slide 8: Conditional (Polled) I/O Transfer
MCU must read status information from the I/O device (1)
Test this status to see if the device is ready for data transfer (2)
  Remain in the wait loop until device is ready
Perform the data transfer (3)
Handshaking is needed
“wait loop”
1
2
3
4
Read I/O device status
Is
device ready
for data transfer
Perform data
transfer operation
Continue
program
No
Yes
Conditional (polled) I/O transfer

## Slide 9: Conditional (Polled) I/O Transfer – E.g.
Type equation here. Converts analog voltage input VA to an 8-bit output (D7-D0)
Conversion process is initiated by a pulse to START
Conversion time, tc can be up to 100s
EOC (end-of-conversion) = LOW during conversion
ENABLE
0
START
0
1
0
Start
Conversion
Conversion
Complete
ENABLE
START
Analog voltage input
8-Bit A/D converter
EOC
8-Bit digital output
Tri-state
outputs
EOC = HIGH when conversion is completed
ENABLE = HIGH, make the latched binary output available
ENABLE = LOW, output at High-Z state (disconnected)
Conditional (polled) I/O transfer

## Slide 10: Conditional (Polled) I/O Transfer – E.g.
Communications between MCU and ADC
  MCU issues a START pulse to the ADC to convert VA to its digital equivalent
  MCU polls the status of EOC output until conversion is completed
  MCU reads the ADC output into one of its internal registers
ENABLE
0
START
0
1
0
Start
Conversion
Conversion
Complete
ENABLE
START
Analog voltage input
8-Bit A/D converter
EOC
8-Bit digital output
Tri-state
outputs
Conditional (polled) I/O transfer

## Slide 11: MCU Initiated – Conditional (Polled) I/O Transfer
Data acquisition subroutine
  May be accessed at any point in the user’s program
Disadvantages
  Need to wait for I/O devices to be ready
  MPU can do other things while waiting, especially when I/O devices are slow

## Slide 12: Device-Initiated Transfer
Interrupt transfer
  Handshaking is required
  I/O device sends a signal to an interrupt input to inform the MCU it is ready for data transfer
  Hardware interrupts are triggered by a state (HIGH/ LOW) or a change in state (HIGH  LOW or LOW  HIGH)
MCU
Interrupt Input
I/O
Device
Data
Interrupt transfer

## Slide 13: Interrupt Transfer
When an interrupt occurs, all the important registers content which define the current state of the MCU are immediately stored away in a dedicated memory location, before going to the ISR
Interrupt Service Routine (ISR)
  Contains commands for transferring to and from the interrupting I/O devices
Upon returning from ISR, MCU returns to the previous state by restoring the contents of the important registers
Setup Commands

Command 1

Command 2
Interrupt 
Command 3

Command 4

Interrupt Service Routine
Interrupt Command 1
Interrupt Command 2
:
Interrupt transfer

## Slide 14: Arduino’s Hardware Interrupts
UNO – INT 0 (Pin 2) & INT 1 (Pin 3)
attachInterrupt(interrupt, ISR, mode)
  interrupt = 0 (Pin 2) or 1 (Pin 3)
  ISR = interrupt service routine must take no parameters and return nothing
  Mode:
    LOW = triggers interrupt when pin is LOW
    CHANGE = triggers interrupt when pin changes state
    RISING = triggers interrupt when pin goes LOWHIGH
    FALLING = triggers interrupt when pin goes HIGHLOW

## Slide 15: Interrupt Service Routine in Arduino
Cannot have parameters and returns nothing
Only 1 ISR can run at any one time, other ISRs (if any) will be turned off until the current one is executed
Functions which rely on timer interrupts will not work while ISR is running, e.g. delay(), millis()
Global variables are used to pass parameters between main program and ISR, i.e. declare them as volatile
Example:
int pin = 1; volatile int state = LOW; void setup(){ pinMode(pin, OUTPUT); attachInterrupt(0, blink, CHANGE);
} void loop(){ digitalWrite(pin, state); } void blink(){ state = !state; }

## Slide 16: Polling vs Interrupting
Advantages of Polling
  Ease of software implementation
Advantages of Interrupting
  Multi-tasking – the MCU can process other commands while waiting for an I/O device to be ready
  Acquisition accuracy – for fast acquisition tasks
    E.g. Reading from an encoder on a fast rotating motor shaft. These pulses are too short for polling method to capture, resulting in missing pulses

## Slide 17: Communications
Parallel data communications
  Multiple bits of data are transmitted all at one time
  One data line/ pin per bit is needed
  Advantage
    Faster data transfer rate
Serial data communications
  Data is transmitted one bit after another
  Only one data line/ pin is needed
  Advantages
    Cheaper to implement, because physical pins/lines are costly
    Easier to integrate into IC & PCB design, because fewer physical pins/lines result in smaller footprint

## Slide 18: Parallel-Serial Interface
  For serial/parallel conversions for communications between MPU and serial I/O device
  Converts a N bit parallel word from the MPU data bus to a serial data word
  Converts a serial data signal from a serial device to an N bit parallel data word
Parallel
data bus
Serial
data
Serial I/O Device
Interface
circuit
MPU
In
Out
Parallel-serial interface

## Slide 19: Universal Asynchronous Receiver Transmitter (UART)
A serial receiver (Rx)
To convert a serial input to a parallel format, and store it in the receiver data register (RxDR) for eventual transmission to MPU
A serial transmitter (Tx)
To take a parallel word from transmitter data register (TxDR) and convert it to a serial format for transmission
A bidirectional data bus buffer
To pass data from MPU to TxDR, or from RxDR to the MPU over system data bus
Baud rate generator
Sometimes external clock is used
MPU
Data bus buffer
RxDR
Receiver (Rx)
TxDR
Transmitter (Tx)
UART
Serial
I/O
Device
Universal Asynchronous Receiver Transmitter (UART)

## Slide 20: Data Transmission Rate
  Bit time interval, TB = period
Baud rate = Data rate = rate of data transmission = 1/TB (bits/s or Mbps)
Common baud rates: 19200, 14400, 9600, etc.
Example: If Data rate = 9600 baud, what is the time duration of 1 bit?
  Data rate = 9600 bits/s
  Bit time = 1/9600 = 104.17 s

## Slide 21: Serial Communication Protocols
Arduino supports two serial communication protocols
  I2C Bus (Asynchronous)
  SPI Bus (Synchronous)
Bus
  Groups of wires used as a common path connecting all the inputs and outputs of several registers/ devices so that data can be easily transferred from any one register/ device to any other using various control signals

## Slide 22: Serial Data Communication
Asynchronous Communication
  Transmitter can send data to receiver at any time
  Time delay between transmission of two words may be indeterminate
  Transmitter clock need not synchronise with receiver clock
Synchronous Communication
  Transmitting and receiving are synchronised by common clock pulses
  Transmitter sends data to receiver continually
  Transmitter sends meaningless data (e.g. sync characters 1616 ASCII) continually when there is no data to send

## Slide 23: I2C Bus
I2C bus is controlled by a master device (MCU)
One or more slave (I/O) devices receive control signal from the master device
All devices share the same clock signal (SCL) and a bidirectional data line (SDA)
Only master device can initiate communications between master and slaves to avoid bus contention
R1
R2
Vcc SDA
Gnd SCL
SDA Vcc
SCL Gnd
SDA Vcc
SCL Gnd
I2C Slave
I2C Slave
I2C Master
5V
Note: pull-up resistors are needed to maintain HIGH state when all devices are disconnected
I2C Bus

## Slide 24: I2C Bus
Each slave device has it own unique 7-bit address or ID number
  Address may be fixed or selectable (manufacturer dependent)
R1
R2
Vcc SDA
Gnd SCL
SDA Vcc
SCL Gnd
SDA Vcc
SCL Gnd
I2C Slave
I2C Slave
I2C Master
5V
When master initiates a communication, a device address is transmitted
Only the slave device with the correct address shall respond to the master
I2C Bus

## Slide 25: I2C Bus – Communication Protocol
Steps to communicate with different I2C slave devices need to follow protocol defined by manufacturer in datasheets
Basic steps:
  Master sends a Start bit
  Master sends a 7-bit slave address of intended device
  Master sends a Read (1) or Write (0) bit depending on application
  Slave responds with an “acknowledge”, i.e. ACK bit (0)
  In Write mode, master sends 1 byte of information (command or data) at a time, and slave respond with ACKs. In Read mode, master receives 1 byte of information at a time and sends an ACK to the slave after each byte
  When communication has been completed, master sends a Stop bit

## Slide 26: SPI Bus
3 pins for communications between master all slaves
Vcc SCLK
MOSI
MISO
SS1
Gnd SS2
SCLK Vcc
MOSI
MISO
SS Gnd
SPI Slave
SPI Slave
SPI Master
5V
SCLK Vcc
MOSI
MISO
SS Gnd
  Shared/Serial Clock (SCLK)
  Master Out Slave In (MOSI)
  Master In Slave Out (MISO)
Total number of I/O pins required = 3 + n n = number of slave devices
Each slave device requires an additional slave select (SS) pin
SPI Bus

## Slide 27: SPI Bus
SPI bus is a full-duplex serial communication protocol between master and one or more slaves
  Full-duplex: Simultaneous bidirectional transmission of information
All slave devices share MOSI, MISO & SCLK lines, hence all commands from master are sent to each slave device
Only the slave device with SS pin set LOW shall respond to master
Vcc SCLK
MOSI
MISO
SS1
Gnd SS2
SCLK Vcc
MOSI
MISO
SS Gnd
SPI Slave
SPI Slave
SPI Master
5V
SCLK Vcc
MOSI
MISO
SS Gnd
SPI Bus

## Slide 28: SPI Bus
SPI devices are synchronous, i.e. data is transmitted in sync with a SCLK
4 modes of communication
Mode | Clock Polarity | Clock Phase (Data capture on …)
0 | Low at idle | Rising Edge
1 | Low at idle | Falling Edge
2 | High at idle | Falling Edge
3 | High at idle | Rising Edge
Vcc SCLK
MOSI
MISO
SS1
Gnd SS2
SCLK Vcc
MOSI
MISO
SS Gnd
SPI Slave
SPI Slave
SPI Master
5V
SCLK Vcc
MOSI
MISO
SS Gnd
SPI Bus

## Slide 29: SPI Bus – Communication Protocol
Basic process:
  Set the SS pin LOW for the targeted slave device
  Toggle SCLK (square wave) at a speed  transmission speed supported by the slave device
  For each clock cycle, master sends 1 bit on MOSI and receives 1 bit on MISO
  Continue until data transmission is complete, and stop toggling the clock line
  Set SS pin to HIGH

## Slide 30: SPI Bus
Every clock cycle a bit must be sent and received (i.e. synchronous), but that bit may be meaningless
Naming conventions (manufacturer dependent)
  Slave Select (SS)  Chip Select (CS)
  Serial Clock (SCLK)  Clock (CLK)
  Master Out Slave In (MOSI)  Serial Data In (SDI)
  Master In Slave Out (MISO)  Serial Data Out (SDO)

## Slide 31: I2C vs SPI
I2C Advantages | SPI Advantages
Requires only 2 communication lines | Higher data transmission rate
 | Easier to implement
 | No pull-up resistors needed

## Slide 32: Summary
Interfacing with I/O devices
  MCU-Initiated
    Unconditional transfer, no handshaking
    Conditional transfer (Polling), handshaking is required
  Device-Initiated
    Interrupt transfer, handshaking is required
    Characteristics of Interrupt Service Routine (ISR)
    Hardware interrupt in Arduino
  Polling vs Interrupting

## Slide 33: Summary
Parallel vs Serial Communications
Universal Asynchronous Receiver Transmitter (UART)
Data transmission rate
Synchronous vs Asynchronous communications
I2C Bus and SPI Bus
  Characteristics, Communication protocols
  Advantages